## Slide 1: DSO-DERA Coordination for the Wholesale Market Participation of Distributed Energy Resources
Authors: Cong Chen1, Ahmed Alahmed1, Subhonmesh Bose3,
Timothy Mount2, and Lang Tong1
1Dept. of Electrical & Computer Engineering, Cornell University, Ithaca, NY, USA
1Dyson School of Applied Economics and Management, Cornell University, Ithaca, NY, USA
2Dept. of Electrical & Computer Engineering, University of Illinois Urbana-Champaign, Urbana (UIUC), IL , USA
09/2023
Wholesale Market Participation of DERA: DSO-DERA Coordination and Competitive DER Aggregation
FERC order 2222
Distributed energy resource aggregator (DERA)
Presenter: Cong Chen
Notes: Hello everyone! My name is Cong Chen. Currently, I’m a Ph.D. candidate in Electrical Engineering from Cornell University supervised by Prof. Lang Tong. Today, I would like to share our research about the wholesale market participation of distributed energy resource aggregator (DERA).
Since 2020, FERC order 2222 began to promote the participation of DERA in the wholesale market. But why we emphasize the coordination problem here? Because most DERA do not own the network. And to participate in the wholesale market, DERA has to coordinate with DSO, the owner of the distribution network. How does multi-DERA share the distribution network? Who should be responsible for the network security? How to formulate a competitive aggregation method as customers can choose from multi-DERA to be aggregated? These are fundamental questions for the coordination of DSO-DERA.

## Slide 2
5kW
-5kW
Day1
Day2
Day3
Network Access
Day1
Day2
Day3
Network Access
A Future Aggregation Model for multi-DERA
Distribution utility and LSE
(DSO)
Retail customers in distribution systems
Power flow (kW)
Financial flow ($)
Wholesale electricity market
(ISO)
DSO customers
Control
DERA1
DERA2
DERA4
DERA3
DSO
Substation
POI
PCC
Transmission grid
Distribution grid
DSO (net) power
DERA1 (net) power
DERA2 (net) power
Line flow limits
Voltage limits
A
Distribution utility and LSE
(DSO)
Retail customers in distribution systems
Power flow (kW)
Financial flow ($)
Wholesale electricity market
(ISO)
DSO customers
DER aggregator (DERA)
DERA customers
Control
DER aggregator (DERA)
DERA customers
(a)
(b)
(c)
Competitive DER aggregation: (a) DERA aggregation model, (b) DERA’s bids in the wholesale market, and (c) DERA’s bids in distribution network access auction.
DSO-DERA-ISO coordination: How do multi-DERA share the power network? How to guarantee reliability?
Notes: We know the structure of power system with ISO, DSO and all retail customers like this. And we envision future there’re multiple DERAs, each has its own customer. Customers have the freedom to choose their incumbent utility company or choose to be aggregated by some DERA. From here we can more clearly see that DSO is responsible to operate physical distribution network power flow represented by the red arrows and ensure the network security and reliability. To participate in the wholesale market, DERA’s power has to by-pass the distribution network to transport the aggregated energy from many end buses to the transmission network.
How does multi-DERA share the distribution network, especially when there are congestions and it’s impossible to know the network security constraint for each DERA? This is challenging.
As for a single DERA, it has interfaces among its customer, the ISO and DSO. To come up with an aggregation algorithm consideration the competition of other DERA is also challenging.

## Slide 3
Literature review and our contribution
  4-tpye DSO-DERA-ISO coordination model
 | Type I | Type II | Type III | Type IV
Feature |  |  |  | 
DSO involvement |  |  |  | 
DSO (net) power
DERA1 (net) power
DERA2 (net) power
Substation
POI
PCC
Transmission grid
Distribution grid
Planning problem:
Solar installation capacity limit
Hosting capacity limit
No control
DER aggregation through DSO
Fully control
Big “DERA”
Local energy market
Fully coordination
Local energy market with distributed LMP
wholesale market LMP
DSO
Our method (access limit allocation)
Ensure network reliability
DERA1
DERA2
DERA4
DERA3
DSO
We decouple DSO-DERA-ISO operations:
As long as the DERA respects allocated access limits, the DSO only needs to manage network reliability for its own customers.
A DERA can exercise its aggregation policy and participate in the wholesale market without considering distribution network constraints.
Notes: We divide the literature about DSO-DERA coordination into 4-types. The first with no DSO control in the realtime is just guarantee the solar installation capacity lower than the hosting capacity limit.
Comparatively, type IV is fully controlled by DERA. It’s completely a DERA aggregation through DSO.
Type III here hopes to establish the local energy market over distribution network the same as the wholesale market with distributed LMP. And DSO coordinate in between. Still, lots of coordination for DSO.
Are there any method to further reduce the coordination burden for DSO, and still efficiently use the network? Our method type II hope to fill this blank. We propose the idea to allocate access limits to DERAs and DSO in the distribution network. At main buses over the distribution network, DSO host a forward auction to partition the total access limit at each bus to different DERAs and DSO. And if everyone stay within the network access limit in the real-time operation, we can decompose the DSO-DERA-ISO operation.
As long as the DERA respects allocated access limits, the DSO only needs to manage network reliability for its own customers.
A DERA can exercise its aggregation policy and participate in the wholesale market without considering distribution network constraints.

## Slide 4
Robust DSO’s network access allocation
  Objectives: Maximize the social welfare while allocating access limits subject to network constraints under all DSO and DERA net-injections
….
Clearing injection access
Clearing withdrawal access
Substation
POI
PCC
Transmission grid
Distribution grid
DSO (net) power
DERA1 (net) power
DERA2 (net) power
DERA1
DERA2
DERA4
DERA3
DSO
Benefit of DERA
Cost of DSO
Maximize …
DERA1
DERA2
DERA4
DERA3
DSO
Locational Marginal Access Price (LMAP)
Notes: Here is the model. In the objective function, we received the bidding benefit from DERA, representing how much DERA is willing to pay for a certain amount of injection and withdrawal access. And we minus the operation cost of DSO to support the total amount of the network access. It’s like social welfare maximization in the wholesale market.
And we clear for both the injection and withdrawal access with these two equations. The total network injection and withdrawal limit equals to the sum of access limit assigned to DSO and DERAs. To realize the decomposition of DSO-DERA coordination, DSO needs to ensure that for any net injection of DSO and DERA, if they stay within the access limit, the power flow and voltage limit should not be violated. Such a “for all” require robust optimization to realize. Luckily, with the linearized power flow model, we have the equivalence of this robust optimization and the optimization can be solved efficiently.
As for the pricing for the network access, we use marginal pricing like LMP, taking the dual variable associate with the equality market clearing conditions and defined as the locational marginal access price
Pause: The DERA don’t need to know the network parameters/topology when coming up its aggregation and bidding strategies. It only needs to stay within the access limit.

## Slide 5
Properties and the simulation result
Proposition 1: DERA nonnegative surplus
Average injection of DSO’s customer
Stoch
Robust
Stoch
20% gain in surplus by tolerating less than 1% constraint violation risk
Average injection of DSO’s customer
Stoch
Robust
Stoch
Proposition 2: DSO revenue adequacy
Proposition 3: Price monotonicity
Notes: For the time limit here, I’ll explain more details about the properties we proved and the simulation in the poster session.
We prove Proposition 1 that the surplus of DERA is nonnegative under certain conditions. And in the simulation we can see over all robust or stochastic case, the DERA surplus is above zero. Mover, comparing the robust and stochastic access allocation mechanism, For DSO surplus. In Proposition 2 we prove the revenue adequacy of DSO.
Lastly, we proved an interesting Proposition 3 for the price monotonicity over one feeder.

## Slide 6
Key take-aways:
Network access allocation mechanism to Multi-DERA
Decouple the operation of DSO-DERA-ISO
Robust and stochastic allocation mechanism
Competitive DER aggregation model
Working paper:
C. Chen, S. Bose, T. D. Mount, and L. Tong, “Wholesale market participation of DERA part I: DSO-DERA-ISO coordination,” [Online], available 2023/07/06) at arXiv: 2307.01999. [Online].
Available: http:// arxiv.org/abs/2307.01999
C. Chen, A. S. Alahmed, T. D. Mount, and L. Tong, “Wholesale market participation of DERA part II: Competitive DER aggregation,” [Online], available 2023/07/06) at arXiv: 2307.02004. [Online].
Available: http:// arxiv.org/abs/2307.02004
Notes: To conclude, the main contribution is that we propose a network allocation mechanism to multi-DERA, which decouple DSO-DERA-ISO operations in the real-time electricity market, ensuring the distribution system reliability independent of DERAs' aggregation actions and wholesale market conditions. To cope with DER uncertainty, we propose the robust and stochastic network access allocation mechanism.
In our paper posted on arXiv, we also develop competitive profit-maximizing aggregation strategies for DERAs and their bidding strategies as virtual storage participants in the wholesale market.